## Slide 1
Map Projections

## Slide 2: What is a Map Projection?
A mathematical expression used to represent the 3D surface of the earth on a 2D map
Always results in distortions
Source: http://support.google.com/earth/bin/answer.py?hl=en&answer=148111

## Slide 3: Projection Surfaces
Cylindrical
  Meridians and parallels are equidistant, straight lines, crossing at right angles
Conical
  Parallel(s) that are touching the cone are assigned unitary scale
Planar
  Point or circle that intersects tangent plane has no distortion
Source: http://en.wikipedia.org/wiki/Map_projection#Projections_by_surface

## Slide 4: Preservation of a Metric Property
Conformal- Preserves angles locally (MapWindow uses this projection exclusively)
Equal-area- Preserves area
Equidistant- Preserves distance from a standard point or line
Gnomonic- Preserves shortest route between two points (great circles projected as straight lines)
Azimuthal- Preserves cardinal directions
Compromise- Balancing/minimizing overall distortion
Source: http://en.wikipedia.org/wiki/Map_projection#Projections_by_surface

## Slide 5: Projection Comparison
Equal Area Projection
Equal Angle Projection

## Slide 6: Universal Transverse Mercator
Lat/Lon WGS84 (UTM) used in Google Earth and MapWindow
Topographical maps, geological maps
Cylindrical, conformal
Large distortions at the poles
Greenland (blue) vs. Africa (red) example
Source: http://support.google.com/earth/bin/answer.py?hl=en&answer=148111
http://www.pratham.name/mercator-projection-africa-vs-greenland.html

## Slide 7: MapWindow Project Projections
Download and extract Map Projections Sample Projects folder Open project in MapWindow > Sample Projects > World > World.mwprj
Click “Ignore Mismatch” if prompted
Assigning a projection to a project: Project > Settings

## Slide 8: MapWindow Project Projections
Click on “Project Projection” and choose the projection you wish to apply to the entire project (may require restart of the project)

## Slide 9: MapWindow Shapefile Projections
Go to the Toolbox tab (or GIS plug-in) to reproject, assign projections, etc. to shapefiles, grids, and/or images

## Slide 17
Add the reprojected shapefile as a map layer to compare projections
Select “Ignore Mismatch” if prompted

## Slide 18: PZ-90 Reprojected Shapefile

## Slide 19: Calculating Area to Compare Projections
Go to the Toolbox > Standard > Calculate Polygon Area

## Slide 20
Layer or shapefile
Name of field in table
Units

## Slide 21
Calculated area of each shape (country) in km^2 using our original projection (WGS84)

## Slide 22
Calculate the area of each country using our reprojected shapefile

## Slide 23
Compare areas (in km^2) of Zaire from two different projections:
WGS84 (1)
Africa Albers Equal Area Conic (2)

## Slide 24
Add a column to the table to display the area in 1000 km^2 (kkm^2)

## Slide 25
New column
Equation

## Slide 26
Compare areas (in kkm^2) of
Greenland from two different projections:
WGS84 (1)
Africa Albers Equal Area Conic (2)

## Slide 28
Different projections calculate different areas for the same country