Paper No.       971050

An ASAE Meeting Presentation

### AUTOMATIC CONTROL SYSTEM FOR VARIABLE RATE CHEMICAL APPLICATION

By

Sreekala Gopalapillai	Lei Tian

## Graduate Research Assistant	Assistant Professor

## Agricultural Engineering Department

University of Illinois

Urbana, IL 61801

Written for presentation at the

1997 ASAE Annual International Meeting

Sponsored by ASAE

Minneapolis Convention Center

Minneapolis, Minnesota

Auust 10-14, 1997

Summary:

A manual flow control system for variable rate application was tested in the laboratory for performance evaluation. It could vary the flow rate in the range of 1:10 with no pressure control and 1:8 at a constant pressure (30 psi), with no significant change in the spray pattern. But the efficiency of field application depended on the operator’s judgement. Based on the same concept of flow control, an automatic controller was developed. The new controller used solenoid valves controlled by 16-bit CPU, 16 MHz controller. It took the weed density data from a vision system and modulated the spray accordingly. The flow rate and spray pattern performances were same as that of the manual control system. But the automatic controller is expected to save more herbicide since it is more precise and accurate.

Keywords:

Variable rate application, flow controller, duty cycle, weed density

The author(s) is solely responsible for the content of this technical presentation. The technical presentation does not necessarily reflect the official position of ASAE, and its printing and distribution does not constitute an endorsement of views which may be expressed.

Technical presentations are not subject to the formal peer review process by ASAE editorial committees; therefore, they are not to be presented as refereed  publications.

Quotation from this work should state that it is from a presentation made by (name of author) at the (listed) ASAE meeting.

EXAMPLE — From Author’s Last Name, Initials. “Title of Presentation.” Presented at the Date and Title of meeting, Paper No X. ASAE, 2950 Niles Road,        St. Joseph, MI 49085-9659 USA.

For information about securing permission to reprint or reproduce a technical presentation, please address inquiries to ASAE.

ASAE, 2950 Niles Rd., St. Joseph, MI 49085-9659 USA

Voice: 616.429.0300      FAX: 616.429.3852      E-Mail:<hq@asae.org>